## Slide 1: The value, challenges and future of performance benchmarking in transport and infrastructure regulation
ITS Research Seminar
Dr Andrew Smith
Institute for Transport Studies, University of Leeds
12th March 2015

## Slide 2: Outline
Principal aims of econometric analysis
Defining efficiency – why use sophisticated econometric techniques?
How can we deal with heterogeneity?
Evidence / impact: rail infrastructure efficiency in Europe (study or ORR)
Evidence / impact: study for Ofwat
Evidence / impact: vertical structure and regulation cost effects (Europe; East Asian Railways)
Conclusions / questions

## Slide 3: Outline
Principal aims of econometric analysis
Defining efficiency – why use sophisticated econometric techniques?
How can we deal with heterogeneity?
Evidence / impact: rail infrastructure efficiency in Europe (study or ORR)
Evidence / impact: study for Ofwat
Evidence / impact: vertical structure and regulation cost effects (Europe; East Asian Railways)
Conclusions / questions

## Slide 4: Any guesses as to what this slide is showing?

## Slide 5: Passenger rail travel in Britain

## Slide 6: Major pressures on railways in Europe
2011 White Paper envisages:
  A 50% shift of medium distance intercity passenger and freight journeys from road to rail and waterborne transport by 2050.
In Britain: the 4Cs
  reduce costs, through improved efficiency, whilst also improving delivering better quality to customers, reducing carbon emissions, and expanding capacity
In an ever more challenging environment

## Slide 7: Much has been achieved in Britain…

## Slide 8: And elsewhere in Europe…

## Slide 9: But…
Much to do
Step changes in performance will be needed
Implies continued and increased focus on efficiency

## Slide 10: Why do econometric analysis?
Benchmarking firms against their peers - efficiency
Economic regulation
Other key sectors: energy, health, communications, postal services…
Studying the impact of reforms (efficiency / productivity)…
20-30% savings European rail (except Britain…)
45% savings in British bus de-regulation
Vertical separation not optimal in all circumstances
What is the optimal size of a rail franchise?
Studying the cost structure of the industry
Scale / density economies?

## Slide 11: Outline
Principal aims of econometric analysis
Defining efficiency – why use sophisticated econometric techniques?
How can we deal with heterogeneity?
Evidence / impact: rail infrastructure efficiency in Europe (study or ORR)
Evidence / impact: study for Ofwat
Evidence / impact: vertical structure and regulation cost effects (Europe; East Asian Railways)
Conclusions / questions

## Slide 12: A starting point for measuring efficiency – unit costs or KPIs
Unit cost measures widely used as a starting point
Cost per track km
KPIs – Key performance indicators

## Slide 13: A starting point for measuring efficiency – unit costs or KPIs
Unit cost measures widely used as a starting point
Problem: which denominator to use?
Econometric methods give a single measure of efficiency that simultaneously takes account of variation in train-km and track-km (and other cost drivers)
An added benefit of econometric methods: important information on scale / density economies
Cost per track km
KPIs – Key performance indicators
Cost per train km

## Slide 14: Why a statistical / econometric model?
Output
Cost
A
O
Efficiency frontier
Firm A has high unit costs – is it inefficient?

## Slide 15: Why a statistical / econometric model?
Output
Cost
A
O
Efficiency frontier

## Slide 16: Why a statistical / econometric model?
Train-km
Cost
A
O
Efficiency frontier
Allow flexibility on the shape of the cost-output relationship (e.g. allow economies of scale)
Allow multiple outputs / other cost drivers (e.g. train and track-km)

## Slide 17: Why a statistical / econometric model?
Cost
A
O
Efficiency frontier
Allow flexibility on the shape of the cost-output relationship (e.g. allow economies of scale)
Allow multiple outputs / other cost drivers (e.g. train and track-km)
Track-km

## Slide 18: Why a statistical / econometric model?
Output
Cost
A
O
Efficiency frontier
Allow flexibility on the shape of the cost-output relationship (e.g. allow economies of scale)
Allow multiple outputs / other cost drivers (e.g. train and track-km)
So we can explain costs in terms of a set of explanatory factors, e.g.
  Network size; traffic density and type; other (e.g. electrification; multiple track); potentially, others…
Having accounted for these factors, and random noise, produce an overall measure of efficiency

## Slide 19: Stochastic Frontier Model
{
{
{
{
Deterministic Frontier
Noise
Inefficiency
Stochastic Frontier
Notes: Deterministic frontier and noise equal the stochastic frontier since this is the frontier the firm actually faces (we simply account for one component using a deterministic representation and an other as noise)

## Slide 20: Outline
Principal aims of econometric analysis
Defining efficiency – why use sophisticated econometric techniques?
How can we deal with heterogeneity?
Evidence / impact: rail infrastructure efficiency in Europe (study or ORR)
Evidence / impact: study for Ofwat
Evidence / impact: vertical structure and regulation cost effects (Europe; East Asian Railways)
Conclusions / questions

## Slide 21: Is transport infrastructure too heterogeneous?

## Slide 22: Modelling differences in characteristics and quality
Simplified representation:
C = f( W, N, Y/N, Z, Q) + error
Network Size
Traffic Density
e.g.
Proportion electrified
Single / multiple track
Capability (speed; axle load)
Topography
Weather…Others
e.g.
Delay minutes
Asset Failures
Track geometry
Asset age
Broken rails
……Others
OBSERVED HETEROGENEITY – MAJOR DATA CHALLENGES
Input prices

## Slide 23: Dealing with unobserved heterogeneity - the literature
Standard Panel: ci is UOH
Schmidt and Sickles (1984): ci re-interpreted (inefficiency)
The question is, how do decompose ci
  Farsi et. al. (2005) – unobserved heterogeneity correlated with regressors; inefficiency is not (see also Mundlak (1978))
  Greene (2005) - unobserved heterogeneity is time invariant; inefficiency is time varying
  Kumbhakar, S. Lien, G. and Hardaker, B. (2014) – use distributional assumptions to decompose time invariant inefficiency and unobserved heterogeneity; and time varying inefficiency and random noise (four component models)
  Regulatory judgement – some kind of “ad-hoc” upper quartile adjustment
Some exciting new models here though few applications in rail yet (I’m working on that!)

## Slide 24: Outline
Principal aims of econometric analysis
Defining efficiency – why use sophisticated econometric techniques?
How can we deal with heterogeneity?
Evidence / impact: rail infrastructure efficiency in Europe (study or ORR)
Evidence / impact: study for Ofwat
Evidence / impact: vertical structure and regulation cost effects (Europe; East Asian Railways)
Conclusions / questions

## Slide 25: International benchmarking study
Panel data:13 European countries over 11 years
Used by International Union of Railways (UIC) in its benchmarking
Standard definitions – to an extent

## Slide 26: International benchmarking study: national data – frontier parameters
Source: Smith (2012)

## Slide 27: Efficiency estimates for Network Rail (PR08)
Implies a gap against the frontier of 40% in 2006
40% gap

## Slide 28: Typical UK regulatory approach
Regulators tend not to use sophisticated methods
Decomposition of noise, unobserved heterogeneity often made via regulatory judgement
Upper quartile adjustment – aim away from the frontier
Timing: ORR also allowed the company ten years to close the gap – so a 40% gap turned into 22% over 5 years (Smith et. al., 2010)
Gap confirmed by bottom-up studies

## Slide 29: Outline
Principal aims of econometric analysis
Defining efficiency – why use sophisticated econometric techniques?
How can we deal with heterogeneity?
Evidence / impact: rail infrastructure efficiency in Europe (study or ORR)
Evidence / impact: study for Ofwat
Evidence / impact: vertical structure and regulation cost effects (Europe; East Asian Railways)
Conclusions / questions

## Slide 30: Study for Ofwat
Builds on work done in rail
Based on econometric model
Bills to fall by 5% in real terms
Tougher than what the companies wanted
Bristol water cut of 21% in real terms (now appealing)
Issue of transparency / complexity
Unobserved heterogeneity

## Slide 31: Outline
Principal aims of econometric analysis
Defining efficiency – why use sophisticated econometric techniques?
How can we deal with heterogeneity?
Evidence / impact: rail infrastructure efficiency in Europe (study or ORR)
Evidence / impact: study for Ofwat
Evidence / impact: vertical structure and regulation cost effects (Europe; East Asian Railways)
Conclusions / questions

## Slide 32: Research questions and contribution
In 2012 European Commission wanted to mandate full, legal separation across Europe
Research questions: does the holding company model have cost saving advantages over vertical separation and in what circumstances?

## Slide 33: Reminder: Holding company model
Infrastructure
Parent or Holding Company
Other
operators
Train Operations
Regulator
Fair Access?
Other
operators

## Slide 34: Reminder: Rationale for holding company model
Internal separation, backed by regulation, gives fair access
Production economies of combining main train operator with infrastructure
Reduced transaction costs
Better alignment of incentives and thus co-ordination benefits

## Slide 35: Measures of heterogeneity
Passenger Output; Freight output
Network size
Technology
Input prices
Load factors
Passenger revenue share
Train length
See Mizutani, F, Smith, A.S.J., Nash, C.A. and Uranishi, S (2014), Comparing the Costs of Vertical Separation, Integration, and Intermediate Organisational Structures in European and East Asian Railways, Journal of Transport Economics and Policy (Fast Track Articles December 2014).
Take account of economies of scale / density before arriving at conclusions

## Slide 36: Findings [1]: the answer all depends on density of usage
Train density
Holding or integrated model is desirable
Vertical separation is
desirable
Break-even point
ΔC of vertical separation c.f. alternatives

## Slide 37: Findings [2]: Commission Policy would raise costs
Notes: Informational asymmetries:
How well informed are voters about decisions taken and their consequences?
Workers in PE suffer from an efficiency drive, but the benefits may not be ver clear to everyone else.
Why not reduce prices below marginal cost. Everyone benefits, but the implications for taxation less transparent.

## Slide 38: What impact does regulation play?
Follows Mizutani, Smith, Nash and Uranishi (2014) model and earlier Mizutani and Uranishi (2013) model
Adds measure of regulation to the study
Theory: direct effect (pressure on costs of infrastructure manager); indirect effect (via enabling greater competition)
Measure of regulation extracted from IBM Rail Liberalisation Index. Covers Europe (2002-2010)

## Slide 39: Impact of regulation results
Smith, Benedetto and Nash, mimeo (2015)
Parameters | Case 1 | Case 2 | Case 3 | Case 4 | Case 5 | Case 6
 | 0.5735*** (0.0829) | - | - | 0.6236*** (0.0936) | - | -
 | - | 0.1695*** (0.0575) | - | - | 0.1840*** (0.0577) | -
 | - | 0.3657*** (0.0466) | - | - | 0.3693*** (0.0463) | -
 | - | - | 0.3102*** (0.0753) | - | - | 0.3516*** (0.0741)
 | - | - | 0.2374*** (0.0549) | - | - | 0.2567*** (0.0549)
 | -0.1941 (0.1489) | - | - | -0.1909 (0.1557) | - | -
 | -0.3608*** (0.0599) | - | - | -0.3073*** (0.0664) | - | -
 | 0.1817*** (0.0299) | - | 0.0991** (0.0507) | 0.1726*** (0.0298) | - | 0.0950** (0.0492)
 | - | - | -0.3899*** (0.0886) | - | - | -0.4348*** (0.0873)
 | 0.0855** (0.0445) | - | 0.3384*** (0.0510) | 0.0713 (0.0456) | - | 0.2907*** (0.0526)
 | -0.1232** (0.0530) | 0.0613 (0.0444) | 0.0499 (0.0525) | -0.1200** (0.0529) | 0.0823* (0.0461) | 0.0741 (0.0527)
 | 0.0423 (0.0937) | -0.2412*** (0.0840) | -0.3278*** (0.0966) | 0.0840 (0.1047) | -0.1515 (0.0964) | -0.2143** (0.1041)
 | - | - | - | -0.0414* (0.0250) | -0.0338** (0.0176) | -0.0684*** (0.0210)
 | - | - | - | 0.0661** (0.0334) | -0.0048 (0.0351) | 0.0584* (0.0336)

## Slide 40: Outline
Principal aims of econometric analysis
Defining efficiency – why use sophisticated econometric techniques?
How can we deal with heterogeneity?
Evidence / impact: rail infrastructure efficiency in Europe (study or ORR)
Evidence / impact: study for Ofwat
Evidence / impact: vertical structure and regulation cost effects (Europe; East Asian Railways)
Conclusions / questions

## Slide 41: Concluding remarks [1]
Econometric modelling of costs produces key information:
  Relative efficiency of firms and impact of reforms
  Optimal cost structure of industries (scale / density)
Policy makers are using the results (e.g. economic regulators; European Commission; UK CMA)
Data is key: heterogeneity and consistency / quality of data). Collecting good quality data takes time and commitment – ideally economic regulators / Ministries need to co-ordinate
New methods to decompose unobserved heterogeneity – for application in railways – incorporate into economic regulation?

## Slide 42: Concluding remarks [2]
Other wider challenges:
  Incorporating measures of quality into the analyses
  Value and cost of resilience (e.g. to climate change)

## Slide 43: Questions / discussion
Thank you for your attention
Questions?
A question from me?
How far could frontier techniques be used more widely in ITS research?
Where there is something that is optimised / maximised / minimised?

## Slide 44
Thank you for your attention
Andrew Smith

## Slide 45: Contact details
Dr Andrew Smith
Institute for Transport Studies (ITS) and Leeds University Business School
Tel (direct): + 44 (0) 113 34 36654
Email: a.s.j.smith@its.leeds.ac.uk
Web site: www.its.leeds.ac.uk

## Slide 46: References
Mizutani, F, Smith, A.S.J., Nash, C.A. and Uranishi, S (2014), Comparing the Costs of Vertical Separation, Integration, and Intermediate Organisational Structures in European and East Asian Railways, Journal of Transport Economics and Policy (Fast Track Articles December 2014).
Smith, A.S.J (2012), ‘The application of stochastic frontier panel models in economic regulation: Experience from the European rail sector’, Transportation Research Part E, 48, pp. 503–515.
Smith, A.S.J., Wheat, P.E. and Smith, G. (2010), ‘The role of international benchmarking in developing rail infrastructure efficiency estimates’, Utilities Policy, vol. 18, 86-93.

## Slide 47: References
Kumbhakar, S.C., Lien, G. and Hardaker, J.B. (2014), ‘Technical efficiency in competing panel data models: a study of Norwegian grain farming’, Journal of Productivity Analysis, 41, 321-37.
Farsi, M., Filippini, M. and Kuenzle, M. 2005. Unobserved heterogeneity in stochastic cost frontier models: an application to Swiss nursing homes. Applied Economics, 37(18): 2127-2141.
Greene, W. (2005), ‘Reconsidering heterogeneity in panel data estimators of the stochastic frontier model’, Journal of Econometrics, vol. 126, pp. 269-303.