Aviation's full climate impact - How to limit it best from an economic and environmental point of view?

Presented by Dr. Janina Scheelhaase, German Aerospace Centre (DLR)

Abstract:

Aviation contributes to climate change by both long-lived CO2 and short-lived non-CO2 effects, such as NOX or contrail cirrus: According to Lee et al. (2009), aircraft-induced CO2 contributed 1.6% to the total anthropogenic radiative forcing in the year 2005. If both CO2 and non-CO2 effects are considered, aviation contributed 4.9% to the total radiative forcing in 2005.

The German Aerospace Centre (DLR) research project AviClim has explored the feasibility for including aviation’s full climate impact in international protocols for climate protection and has investigated the economic impacts. In AviClim four reduction scenarios have been designed which differ concerning the level of international support for climate protecting measures. These scenarios have been combined alternatively with an emissions trading scheme on CO2 and non-CO2 species, a climate tax and a NOX emission charge combined with operational measures (such as climate-optimized flight paths). This presentation provides an overview of the main results of this research project.

Bio:

(MBA, PhD) is an Environmental Economist at DLR and a specialist for Emissions Trading and Aviation. She is Head of Air Transport Economics at the DLR Institute of Air Transport and Airport Research. She has led and conducted more than 30 both national and international projects in the areas of environmental and economic policy during the last 20 years. She was a member of ICAO CAEP/7 Emission Trading Task Force (on behalf of the German Federal Ministry for Transport) for three years (2005-2007) and co-author of the ICAO CAEP “Guidance on Emissions Trading for Aviation”. Also, she is a member of the ECAC/ANCAT Sub-Group on Emissions Trading for aviation since 2005 as well as a founding member of the ACARE Emissions Trading Group in 2006. On behalf of the German Federal Ministry of Research she has been heading a research project on the economic and environmental impacts of market-based measures for regulating aviation’s full climate impact in the timeframe 10/2011 – 3/2015. She is the author of fifteen technical books, partly with co-authors, on environmental economic issues and more than fifty technical articles, mostly published in refereed journals.